## Slide 1
Colin Clark
Shoreland Zoning Coordinator
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION
Protecting Maine’s Air, Land and Water
Shoreland Zoning Guidelines
KVCOG Shoreland Zoning Training
2024
Notes: Introduction: DEP, SZ

## Slide 2: Shoreland Zoning Applicability
Great ponds
Streams
Rivers
Coastal wetlands
Freshwater wetlands
(all defined, and all
depicted on SLZ map)
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Great ponds have surface area of 10+ acres or 30+ acre impoundments.
Streams start at the confluence of two perennial streams or the outlet of a great pond
Rivers begin where it drains 25 square miles
Coastal wetlands include all areas below the highest annual tide, including tidal portions of rivers.
Freshwater wetlands are 10+ acre wetlands

## Slide 3
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Remember to always refer to the local shoreland zoning ordinance and map!
Note that intermittent and perennial streams have no shoreland zone.
The shoreland zone of streams is only 75 feet from the shoreline.
Within the shoreland zone, tributary streams do not have their own shoreland zone but there are setback requirements from their shoreline.
Wetland areas that are contiguous with great pond and rivers are part of great ponds and rivers, and the shoreline is measured as the upland edge of those wetland areas. Rivers also include floodplain wetlands.

## Slide 4: Shoreline Setbacks for Structures
Setback depends on resource, use and district:
Great ponds and rivers to great ponds 100ft
Other rivers, streams and wetlands 75ft
Tributary streams (within shoreland zone) 75ft
General Development II District 75ft
General Development I District 25ft
Functionally water-dependent uses 0ft
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Uses not allowed in RP effectively have a 250-foot setback.
Describe GD I & II
CFMA designed for only functionally water-dependent uses, so no setback.

## Slide 5: Amendment Process
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Who will be involved:
Planning board or a committee task?
Appoint a drafter (computer user)
Other officials, for getting public input?
Assistance from shoreland staff:
Review draft amendment language
Discuss pros and cons of various options
Advise on any necessary map amendments
Notes: DEP can provide draft language and additional options that are not contained in the 2015 Guidelines

## Slide 6: Local Procedures
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Determine timeline, work backwards from:
Date of adoption (town meeting / council vote)
Warrant/agenda deadline
Required public hearing
Public/individual notices
PB consideration/passage?
Map refinement
DEP draft review?
Map drafted
Ordinance drafted
Notes: Shoreland staff can review drafts upon request, serve as translators between officials and mappers, guide the mapper to data needed

## Slide 7: Following Through
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
After local adoption:
Submit copy of amendments, attested by the clerk
45-day review period
Receive DEP Order
Contact Maine Forest Service
If conditional approval:
Notice of DEP Order first
  Contact shoreland staff with concerns
Attach conditions to ordinance
Notes: Hard copies. Either identified amendments or statement of full ordinance submitted for review. Map size.
Review period begins upon receipt of attested copies.
Shoreland staff notify MFS of option, but if option 2 then contact MFS for agreement.
Don’t make changes required by conditions, that requires adoption, just attach conditions for administration.

## Slide 8: Minimum Lot Standards
Minimum lot standards required for each principal structure and/or use
Lot area
Minimum lot width
Shore frontage
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Lot standards include lot area, lot width and shore frontage. The minimums are required for each and every principal use.
Lot area does not include the land below the shoreline and beneath a road.
Lot width is measured as the closest distance between the two side lot lines everywhere within 100 feet of the shoreline.
Shore frontage is measured in a straight line between the intersections of lot lines with the shoreline, not like realty measurement.

## Slide 9: Lot Area
Required lot area depends on:
Proposed use
Type of resource (tidal vs. non-)
CFMA district designation
Lot area defined:
Excludes land below the shoreline
Excludes land w/in a wetland
Excludes land beneath a road
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Lot area required per principal structure/use
Lot area does not necessarily equate taxed or deeded land area

## Slide 10: Lot Width
Minimum lot width:
Measured as closest distance between the side lot lines
Applies within 100 feet of the shoreline
Varies with shore frontage requirements
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Any portion of the lot within 100 feet must meet the requirement, not just one point within 100 feet.
Lot does not have to include / be on the shoreline.

## Slide 11: Shore Frontage
Shore frontage required:
Varies with lot area requirements
Measured in a straight line between the intersections of the lot lines with the shoreline
Not the same as realty frontage
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Purpose of shore frontage standard

## Slide 12: Measuring Setback
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Nearest horizontal distance from the shoreline to nearest part of the structure or other regulated area
Notes: Nearest means the measurement is not necessary perpendicular to shoreline or structure.
Setback is not measured along the ground.
Nearest part of a dwelling is often the eves, patio or deck.

## Slide 13: Height of a Structure
Defined as:
Vertical distance between the mean original (prior to construction) grade at the downhill side of the structure and the highest point of the structure
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: In most districts, the height limit is 35 feet.

## Slide 14: Height of a Structure In Area of Special Flood Hazard 38 MRSA §439-A (4)(C-1)
“Notwithstanding the limitations on height imposed under paragraphs B and C, (footprint expansion sections) the height of a structure that is a legally existing nonconforming principal or accessory structure may be raised to, but not above, the minimum elevation necessary to be consistent with the local floodplain management elevation requirement or to 3 feet above base flood elevation, whichever is greater as long as the structure is relocated, reconstructed, replaced or elevated within the boundaries of the parcel so that the water body or wetland setback requirement is met to the greatest practical extent.
This paragraph applies to structures that:
Have been or are proposed to be relocated, reconstructed, replaced or elevated to be consistent with the local floodplain management elevation requirement; and
Are located in an area of special flood hazard.
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: In most districts, the height limit is 35 feet.

## Slide 15: Height of a Structure In Area of Special Flood Hazard
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
38 MRSA § 436-A (1-C)
Area of special flood hazard means land in a floodplain having a 1% or greater chance of flooding in any given year, as identified in the effective federal flood insurance study and corresponding flood insurance rate maps.
38 MRSA § 436-A (7-A)
Height means with respect to existing principal or accessory structures, including legally existing nonconforming structures, located within and area of special flood hazard that have been or are proposed to be relocated, reconstructed, replaces or elevated to be consistent with the minimum elevation required by a local floodplain management ordinance, the vertical distance between the bottom of the sill of the structure to the highest point of the structure, excluding chimneys, steeples, antennas and similar appurtenances that have no floor area.
Notes: In most districts, the height limit is 35 feet.

## Slide 16: Height of a Structure In Area of Special Flood Hazard
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: In most districts, the height limit is 35 feet.

## Slide 17
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Nonconforming Structures
Legally existing nonconforming structures can be maintained
Legally existing nonconforming structures can be expanded
Relocation requires setback be met to the greatest practical extent
Destruction, removal or damage of more than 50% of the market value of a structure requires relocation to meet structure setback to the greatest practical extent

## Slide 18: Reconstruction Standards
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
In-place reconstruction/replacement if:
< 50% of the market value of the structure is removed, damaged, or destroyed
Relocation required if:
> 50% of the market
value of the structure
is removed, damaged,
or destroyed
Notes: Most projects are obvious, but use your professional judgement.
The applicant has the burden of proof.

## Slide 19: How does one consider “market value”?
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Market value relates ONLY to the value of the non-conforming structure. The structure has the exact same value whether it is located such that there is a ‘million dollar view’, or it is located next to the town landfill.
Notes: Many structures are nonconforming to setbacks

## Slide 20: What else about the 50% market value threshold?
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
“…which is removed, or damaged or destroyed, regardless of the cause, by more than 50% of the market value of the structure before such damage, destruction or removal…”
Does NOT take into consideration material or labor costs
Does NOT apply to basic repair & maintenance (e.g. re-shingling roof)
Consider all elements of projects (e.g. removing roof, sills due to rot, walls due to mold, windows, doors, etc), but avoid absurdity (e.g. removing 2 coats of paint)!
Notes: Many structures are nonconforming to setbacks

## Slide 21: Relocation Review
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
When relocation is required:
The reviewing authority determines where the existing structure could be relocated to meet the setback to the greatest practical extent
Criteria for making this determination includes:
Characteristics of the land and lot
Locations of existing structures
Existing and future septic systems
The condition of existing foundation
Seek advisory opinions
Notes: Make sure the application demonstrates all limitations to meeting the setback.
Criteria can be tricky or subjective, so seek assistance when needed.

## Slide 22: Relocation First
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Not Greatest Practical Extent
Relocate original structure
to meet setback
Notes: When expansion is proposed, and relocation is proposed or required, then the relocation evaluation is done before expansion is considered.
Ordinances amended since 2006 require the original location to be revegetated.

## Slide 23: NEW!! Footprint and Height Method
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Change from floor area and volume to “footprint” and height- tiered, based on distance from shore
Landowners choose between the cap limit or 30% for footprint, and existing height or height cap
Plans recorded at registry of deeds
Municipal officials may choose to:
Limit expansions by the caps or by 30%, instead of allowing landowner choice
Allow limited expansions within 25 feet of the shoreline
Allow limited expansions in Resource Protection District
Notes: Difference b/t floor area and footprint
Difference b/t volume and height

## Slide 24: What is “Footprint”?
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Footprint - the entire area of ground covered by the structure(s) on a lot, including but not limited to cantilevered or similar overhanging extensions, as well as unenclosed structures, such as patios and decks

## Slide 25: Other Definitions using “Footprint”
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Expansion of a structure, change floor area & volume
Expansion of a use, change floor area
Floor area, remove reference to unenclosed structures
Nonconforming structure, add footprint

## Slide 26
Footprint expansion-highlights
25 feet
100 feet
No expansion unless principal structure entirely w/in 25’, then 800 sf or 30%. No accessory structure expansion.
Height- existing, or max height:
15 ft
Great Pond
75 feet
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 27
Footprint expansion- highlights
25 feet
100 feet
No expansion unless principal structure entirely w/in 25’, then 800 sf or 30%. No accessory structure expansion.
Height- existing, or max height:
20 ft
15 ft
Great Pond
75 feet
Expansion up to 1,000 sf, or 30%, whichever is greater (maximum combined total footprint). No accessory structure expansion if closer to shoreline than principal structure.
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 28
Footprint expansion- highlights
25 feet
100 feet
No expansion unless principal structure entirely w/in 25’, then 800 sf or 30%. No accessory structure expansion.
Height- existing, or max height:
20 ft
15 ft
Great Pond
75 feet
Expansion up to 1,000 sf, or 30%, whichever is greater (maximum combined total footprint). No accessory structure expansion if closer to shoreline than principal structure.
Expansion up to 1,500 sf, or 30%, whichever is greater (maximum combined total footprint). No accessory structure expansion if closer to shoreline than principal structure.
25 ft
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 29
Footprint expansion- highlights
25 feet
No expansion unless principal structure entirely w/in 25’, then 800 sf or 30%. No accessory structure expansion.
Height- existing, or max height:
20 ft
15 ft
Coastal or Freshwater Wetland, River, Stream, Tributary Stream
75 feet
Expansion up to 1,000 sf, or 30%, whichever is greater (maximum combined total footprint). No accessory structure expansion if closer to shoreline than principal structure.
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 30
Footprint expansion- highlights
Resource Protection District
75 feet
250 feet
Same expansion thresholds as for other districts
Height- existing, or max height:
25 ft
Great Pond
Expansion up to 1,500 sf, or 30%, whichever is greater (maximum combined total footprint). No accessory structure expansion if closer to shoreline than principal structure.
15 or 20 ft
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 31
1) What can be expanded?
25 feet
100 feet
800 sf cap or 30%
800 sf camp
200 sf
shed
500 sf
garage
25 ft
20 ft
15 ft
Great Pond
75 feet
Height- existing, or max height:
1000 sf cap or 30%
1500 sf cap or 30%
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 32
800 sf camp
1) Answer: rear of camp or shed (30%), and garage
25 feet
100 feet
800 sf cap or 30%
200 sf
shed
500 sf
garage
25 ft
20 ft
15 ft
Great Pond
75 feet
Height- existing, or max height:
1000 sf cap or 30%
1500 sf cap or 30%
no expansion
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 33
2) What can be expanded?
25 feet
100 feet
800 sf cap or 30%
800 sf camp
200 sf
shed
500 sf
garage
25 ft
20 ft
15 ft
Great Pond
75 feet
Height- existing, or max height:
1000 sf cap or 30%
1500 sf cap or 30%
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 34
2) Answer: camp and/or shed (30%).
Camp cannot add garage footprint.
25 feet
100 feet
800 sf cap or 30%
800 sf camp
200 sf
shed
500 sf
garage
25 ft
20 ft
15 ft
Great Pond
75 feet
Height- existing, or max height:
1000 sf cap or 30%
1500 sf cap or 30%
Accessory structures <25’: no expansion
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 35
3) What can be expanded?
25 feet
100 feet
800 sf cap or 30%
800 sf camp
200 sf
shed
500 sf
garage
25 ft
20 ft
15 ft
Great Pond
75 feet
Height- existing, or max height:
1000 sf cap or 30%
1500 sf cap or 30%
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 36
3) Answer: camp only (30% of total footprint
of all structures)
25 feet
100 feet
800 sf cap or 30%
800 sf camp
200 sf
shed
500 sf
garage
25 ft
20 ft
15 ft
Great Pond
75 feet
Height- existing, or max height:
1000 sf cap or 30%
1500 sf cap or 30%
accessory structures closer than principal structure: no expansion
accessory w/in 25’: no expansion
Notes: This rule is an option for the town to adopt and then administer in place of 30% rule.

## Slide 37: Functionally Water-Dependent
Primary purpose requires location on or direct access to waters and cannot be located away from these waters
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Structures and uses that are functionally water-dependent are not required to meet shoreline setbacks.
Helps protect commercial fisheries and maritime activities, and conserve points of access to waters.

## Slide 38: Definition
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Functionally water-dependent:
Includes fish-related storage
Include shoreline structures necessary for erosion control purposes (in place of retaining walls)
Excludes recreational boat storage buildings (boat house)
Notes: To be consistent with revisions in the Act

## Slide 39: Setback Violations
If it looks like a duck…
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Common violations involve decks on the shoreline.
Others include patios and walkways within the shoreline setback area.
Newer violations include moored or docked structures (not watercraft)

## Slide 40: Non-vegetated surfaces aka ‘lot coverage’
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
The total footprint area of all non-vegetated surfaces within the shoreland zone is limited (note that it does not say “impervious surfaces”).
Unintentional violations occur because the assumptions is often that it is impervious surface. This includes exposed ledge.
Notes: Not just impervious surfaces.
Municipal officials may choose to include any or all of these exemptions from being included in the measurement of total non-vegetated surfaces

## Slide 41: Non-vegetated Surfaces- aka: Lot Coverage
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Surfaces include:
Structures
Driveways*
Parking areas*
Other areas from which vegetation was removed
Optional exemptions:
Naturally occurring ledge and rock outcroppings on lots existing on 3/24/90
Public boat launching facilities
*No exemption for grass paver type products
Notes: Not just impervious surfaces.
Municipal officials may choose to include any or all of these exemptions from being included in the measurement of total non-vegetated surfaces

## Slide 42: Naturally Occurring Ledge…
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep

## Slide 43: Grass Paver Products- Question
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Can a municipal Code Enforcement Officer or planning board exempt areas using grass paver types of products from the lot coverage limitation?

## Slide 44
Grass (?) pavers…
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep

## Slide 45: Non-Vegetated Surfaces
Total area is limited as percentage of lot area:
20% in most shoreland zone districts
70% in shoreland zone of coastal wetlands and rivers not flowing to great ponds where district is CFMA or GD
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Purpose
Prevent unintentional violations by requiring depiction on site plans
This standard often varies municipality to municipality

## Slide 46
Non-vegetated surfaces…
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep

## Slide 47: Vegetation Purposes
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Vegetation is the cheap and natural way to:
Intercept and infiltrate stormwater runoff
Slow and control soil erosion and sedimentation
Provide bird & wildlife habitat, and shade aquatic habitat
Keep privacy and conserve natural character of Maine
Notes: Vegetation standards help achieve shoreland purposes

## Slide 48: Shoreline Buffer Standards
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Removal of vegetation is limited:
Within 100ft of great ponds & rivers flowing to great pond
Within 75ft of other rivers, streams and wetlands
Within 75ft of tributary streams (in the shoreland zone)
To canopy openings of less than 250 square feet
To a single meandering footpath
no wider than 6 ft;
To removing trees and saplings
based on a plot/point system;
To pruning live branches only
the bottom third of trees
Notes: Help prevent unintentional violations by remembering that the setback is often the same as the buffer requirement
The plot system assigns points to trees based on diameter, and requires a certain number of points and saplings for each plot

## Slide 49: Buffer Point System Well-Distributed Stand
25x50 plot area
24 points for great ponds, and rivers and streams flowing to great ponds
16 points for other waterbodies/wetlands
DBH (inches) Points
2<4 1
4<8 2
8<12 4
12 + 8
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: A town has one or the other plot size, so points vary town to town. Plots are set up in area to be cleared. No clearing allowed if minimum points are not had.

## Slide 50
Buffer Point System
>12” DBH = 8 points
>4”, <8”= 2 points
>2”, <4” = 1 point
Great Pond
25’
50’
>8”, <12”= 4 points
2 x 8 = 16 points
3 x 2 = 6 points
5 x 1 = 5 points
35 points
2 x 4 = 8 points
2 x 8 = 16 points
2 x 2 = 4 points
4 x 1 = 4 points
28 points
1 x 4 = 4 points

## Slide 51: Buffer cut according to standards…
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep

## Slide 52
No cleared openings greater than 250 square feet within setback
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Within the setback

## Slide 53: Vegetated Buffers Footpath/Staircase allowed Vegetation Plan
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: A 6-foot wide, meandering footpath is allowed through the vegetated buffer for shoreline access. Any base material added, such as gravel or peastone, makes the path a structure as defined and is strongly discouraged.
The plot system using tree points can be complicated, and then having to investigate a complaint can be time-consuming. Most violations are clearly violations; still, it’s a good idea to encourage landowners to maintain a vegetation plan even when permitting is not required. The plan would show what vegetation they had, where they set up plots, and what vegetation they removed, and when.

## Slide 54: Hazard Tree Defined
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Definition for hazard tree:
structural defect…
under the normal range of environmental conditions, not:
  hurricanes, hurricane-force winds,
  tornados, microbursts, or
  significant ice storm events
exhibits a high probability of failure…
will strike a target.
  Area where personal injury or property damage could occur
  roads, driveways, parking areas, structures, campsites, and any other developed area where people frequently gather and linger
also trees that pose imminent risk to bank stability.
Notes: Defect that would result in failure under normal conditions, AND will strike a target. Without a target, it is not a hazard tree, except for trees posing a serious and imminent risk to bank stability.

## Slide 55: Hazard Trees
Within shoreline buffer:
Replace tree canopy opening > 250sf
  new tree growth present or
  Plant native trees at least 4ft in height and 2in DBH
No stump removal
CEO may require:
Professional evaluation
>1:1 for >8in DBH trees
Outside buffer:
Replace if tree volume or cleared openings exceeded
With new tree growth or
  With native trees at least 2in DBH
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Consultation with CEO required
Municipal officials may choose to make standards more restrictive

## Slide 56: Dead Trees
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Dead trees – contain no foliage during the growing season:
Removal allowed if dead from natural causes
No creation of new lawn areas or other permanently cleared areas
No stump removal
Notes: No permit or consultation
Municipal officials may choose to make standards more restrictive

## Slide 57: Storm-Damaged Tree Definition
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Definition for storm-damaged tree:
a tree that is damaged beyond the point of recovery
as a result of a storm event.
Could be uprooted, blown down, lying on the ground, or still standing

## Slide 58: Storm-Damaged Trees
Within shoreline buffer:
Pruning damaged limbs above 1/3 allowed
Replace tree canopy opening > 250sf
  By natural regeneration or
  With native seedlings or saplings, 1 per 80sf
No creation of new lawn or other cleared areas
No stump removal
Outside buffer:
Replace tree volume or cleared openings
  By natural regeneration
  With native seedlings or saplings on 1:1 basis
Regeneration must occur within 1 season
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Notes: Consultation with CEO required
Municipal officials may choose to make standards more restrictive

## Slide 59: Administration: Disability Variances
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
Municipal officials may choose to:
Allow the CEO to issue a permit and disability variance for making dwelling accessible to person with disability
Please remember, required notices to DEP, just like any other variance!
Notes: Alternatively, separate state statute gives board of appeals the authority to issue disability variance

## Slide 60: NRPA vs. SLZ
NRPA administered by DEP
SLZ administered by municipality
NRPA applies to all field identified resources as defined
SLZ only applies to mapped resources as defined
NRPA more resources covered but lesser setbacks generally
SLZ fewer streams and wetlands but greater setbacks generally
NRPA adjacency standards vary from SLZ buffer standards
NRPA purpose includes water quality and habitat protection
SLZ additional purposes include development density, traditional land use, flooding and aesthetics.
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep

## Slide 61: Basic Review Standards- Question
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
If DEP issues a permit under the Natural Resources Protection Act (NRPA), can a municipality approve a project on that basis?
Notes: If it appears that a dimensional standard cannot be met legitimately, refer the applicant to the board of appeals.
FOF are required when denying applications, but it is also a good idea when you approve applications in case of any aggrieved party

## Slide 62: NRPA & SLZ
MAINE DEPARTMENT OF ENVIRONMENTAL PROTECTION www.maine.gov/dep
If DEP approves a Permit by Rule or other permit under the NRPA, a project must still separately comply with all shoreland zoning provisions in order for the municipality to grant a shoreland zoning permit.
Notes: This means that if a project is approved by the Department, it still needs to be reviewed to meet local shoreland zoning standards.

## Slide 63
Shoreland Zoning Program
Notes: Please don’t hesitate to call us when you have questions.